## Slide 1: RISC-V Standard C Extensions(RVC) Compiler Implementation
Reza Yazdani
November 2020

## Slide 2: Content
What is “C” Standard Extension
Example
16-bit code generation steps
C convertible instructions
Transformation Phases
Implementation Steps

## Slide 3: Compressed Instruction Philosophy & Benefit
Reduction of code size for embedded applications
Improve performance and energy-efficiency for all applications due to fewer misses in the instruction cache
Instruction fetch bandwidth can be a major bottleneck in servers running commercial workloads, which often have a large instruction working set
RVC fetches 25%-30% fewer instruction bits. Reduces instruction cache misses by 20%-25%, or roughly the same performance impact as doubling the instruction cache size
C extension is not a stand-alone ISA, and is meant to be used alongside a base ISA.

## Slide 4: “C” Compressed Instruction (RVC)
Goal is reduction of the code size by:
- adding short 16-bit instruction encodings for common operations
- making it a two address instructions (e.g. s0 += s1 or s0  s0+s1)
C extension is a stand-alone ISA. It is meant to be used alongside a base ISA.
The C extension can be used with RV32, RV64, RV128
50%–60% of the RISC-V instructions can be replaced with RVC instructions
25%–30% code-size reduction.
16-bit instructions can be freely intermixed with 32-bit instructions.
“Compilers can be unaware of the RVC extension and leave code compression to the assembler and linker, although a compression-aware compiler will generally be able to produce better results.”

## Slide 5: “C” registers
000 | 001 | 010 | 011 | 100 | 101 | 110 | 111
x8 | x9 | x10 | x11 | x12 | x13 | x14 | x15
s0 | s1 | s2 | s3 | s4 | s5 | s6 | s7
f8 | f9 | f10 | f11 | f12 | f13 | f14 | f15
fs0 | fs1 | fs2 | fs3 | fs4 | fs5 | fs6 | fs7
RVC Registers
Integer Registers
Integer Registers ABI Names
Floating-Point Registers
Floating-Point Registers ABI Names

## Slide 6: Example: A = (B+C) + (D+E)
In 32-bit format: A = (B+C); X=(D+E); A = A + X where X is a temporary registers. In 32 bit. Total of 96 bits
“C” format: A = (B+C); X =(D+E); A += X. Only A += X is 16-bit. Total 80 bits
“C” format optimal: A = (B+C); A += D; A += E. Only A = B + C is 32-bit. Total 64 bits.
A
A
C
B
X
E
D
32
32
32
A
A
C
B
X
E
D
32
32
16
B
A
A
A
C
D
B
32
16
16
Base
C format
C format optimal

## Slide 7: 16-bit code generation steps
Generate Base code
Identification of instructions to be converted to C (16 bit)
Transformation of identified instructions to comply with C-extension’s constraints (e.g. creation of two address instructions)
Register Allocation with copy elimination
C code generation
Branch offset correction

## Slide 8: C convertible instruction groups
Directly convertible from 32 bit to 16-bit format without any change (e.g. load from stack with five bits offset).
Two address instructions like ADDI(rd, rs, imm) that adds a 6-bit imm to a register. The register can be any of 32 registers. Source and target must be the same in C.
Instructions such as ADD(rd, rs1, rs2). In C format rd must be the same as rs1. The register can be any of 32 registers.
Instructions such as AND(rd, rs1, rs2). In C format rd must be the same as rs1 and rd and rs2 must be registers x8-x15

## Slide 9: Transformation Phases
Phase 1:Transformation of Base
Phase2: Register Allocation with copy elimination
Phase3: Copy elimination
Phase 4: 16-bit instruction generation
Phase 5: Branch adjustment

## Slide 10: Notes on V8 Register Allocator
Inserts constraints “ResolvePhis” lowers phis to “mov’s”
Inserting constraints before register allocation means that the operands participating in the moves must be considered when performing liveness analysis
In last phase of register allocator:
  Pushes downwards moves within a block, as long as that preserves semantics,
  Merges moves common to all last instructions of all predecessors of a block

## Slide 11: Phase 1:Transformation of Base
Mark instruction conforming to C extension without any change
Generate mov(rd, rs1) and X(rd, rd, imm) for X(rd, rs, imm) in group “b”
Generate mov(rd, rs1) and Y(rd, rd, rs2) for Y(rd, rs1, rs2) in group “c”
Generate mov(rd, rs1) and Z(rd, rd, rs2) for Z(rd, rs1, rs2) in group “d”. Mark rd, rs1 and rs2 to be assigned to x8-x15 registers

## Slide 12: Phase2: Register Allocation with copy elimination
While coloring, color candidates marked as x8-x15 candidates if available.
Assign rd and rs in mov(rd, rs) to the same register if possible.

## Slide 13: Phase3: Copy elimination
Eliminate mov’s that source and target are the same registers from the instruction set
If a mov(rd, rs) is not eliminated and is generated in transformation phase copy forward rs to rd and eliminate the move

## Slide 14: Phase 4: 16-bit instruction generation
Instructions that directly go from 32 bit to 16-bit format without any change (e.g. load from stack with five bits offset) are replaced with 16-bit instructions
Two register address instructions like ADDI(rd, rd, imm) in group b replaced with C extension equivalent
3 registers instructions X(rd,rd,rs2) in group “c” are converted to 16
3 registers instructions Y(rd,rd,rs2) in group “d” are converted if both rd and rs2 are registers x8-x15

## Slide 15: Phase 5: Branch adjustment
Calculate sum of 16 bits and 32-bit instructions between branch and the target as new branch offset. 32-bit instructions are counted as 2 and 16-bits as 1

## Slide 16: Implementation Steps
Define16-bit instructions
  make 32-bit instructions point to their 16-bit counterparts
  define rules to reduce 32-bit to 16=bit as part of the 32-bit definition
  automatically generate required changes in a pass through instructions before register allocation
Register allocation with copy elimination
Register copy propagation and elimination
Regeneration of 32-bit instructions in 16-bit (“C” format)